## Slide 1
DESIGN & SIMULATION OF MICROPROCESSORS USING A FULL ADDER
From RISC-V architecture to gate-level implementation
Student: ____________________ Roll No.: ____________________ Department / College: ____________________
REGISTER FILE
ALU / ADDER
CONTROL UNIT
LOGIC GATES

## Slide 2
Introduction and objectives
OVERVIEW
DESIGN & SIMULATION OF MICROPROCESSORS | 02
• Microprocessors execute instructions by moving and transforming binary data.
• A full adder adds three one-bit inputs and produces a sum bit and a carry bit.
• Objective: design the logic, simulate all input combinations, and verify correctness.
• Connect the circuit to the ALU and the six modules of Computer Organization and Digital Logic.
Project focus
A full adder is an arithmetic building block—not a complete microprocessor.

## Slide 3
M1 — The whole computer
CO1
DESIGN & SIMULATION OF MICROPROCESSORS | 03
Stored-program model
Instructions and data are encoded as bits in memory. The CPU fetches, decodes, and executes instructions.
Main CPU blocks
Program counter, instruction memory, register file, control unit, ALU, and data memory.
Where the adder fits
The ALU uses arithmetic circuitry to calculate results for instructions such as ADD and SUB.
High-level view
Memory
Control
Register file
ALU
→
→
→

## Slide 4
M1 — RISC-V ISA and fetch–decode–execute
CO1
DESIGN & SIMULATION OF MICROPROCESSORS | 04
ISA = hardware/software contract
Defines instruction behavior and register-visible results. RISC-V includes add, sub, and, or, slt, addi, lw, sw, beq, and jal.
Instruction example
add x5, x6, x7 Meaning: x5 ← x6 + x7.
• Fetch: read the instruction at the address held by the PC.
• Decode: identify the opcode, registers, and operation.
• Execute: the ALU adds the operand values.
• Write-back: save the result in the destination register.
• Binary and hexadecimal make machine instructions and data easier to inspect; two's complement represents signed integers.

## Slide 5
M2 — Single-cycle datapath
CO2
DESIGN & SIMULATION OF MICROPROCESSORS | 05
Register file
ALU
Write-back mux
Destination register
→
→
→
Data path
Operands travel from registers to the ALU. The computed result passes through write-back to the destination register.
Other CPU paths
The full datapath also contains the PC, instruction memory, control signals, and paths for loads, stores, and branches.
Conceptual diagram; exact wiring depends on the selected RISC-V subset and implementation.

## Slide 6
M2 — Control unit and ALU operations
CO2
DESIGN & SIMULATION OF MICROPROCESSORS | 06
• The control unit decodes the instruction opcode and function fields.
• Control signals select the ALU operation, register write, memory access, and multiplexer paths.
• ADD selects addition; SUB selects subtraction; AND and OR select bitwise logic; SLT compares signed values.
• The full adder provides the core bit-level arithmetic used by an adder/subtractor circuit.
• Control decides which operation is required; the arithmetic circuit computes the output.
Key distinction
The full adder is part of the datapath; it is not the instruction decoder.

## Slide 7
M3 — Memory and register file
CO3
DESIGN & SIMULATION OF MICROPROCESSORS | 07
Register file
A small, fast collection of CPU registers. Typically reads two source operands and writes one result per clock in a simple datapath.
Memory
Instruction memory supplies program instructions; data memory stores values accessed by load and store instructions.
Example operand flow
x6 = 5 + x7 = 3 → ALU → x5 = 8
The register file supplies values; the ALU calculates; write-back stores the result.

## Slide 8
M3 — Memory hierarchy and data flow
CO3
DESIGN & SIMULATION OF MICROPROCESSORS | 08
Registers
Smallest and fastest; hold active operands
Cache
Keeps recently/frequently used data close to CPU
Main memory (RAM)
Larger working store; slower than cache
Secondary storage
Persistent, large-capacity storage
The full adder calculates values; memory hierarchy determines where instructions and data are stored and how quickly they can be accessed.

## Slide 9
M4 — Sequential logic and state
CO4
DESIGN & SIMULATION OF MICROPROCESSORS | 09
Combinational circuit
Outputs depend on current inputs. A full adder is combinational: change A, B, or Cin and its outputs respond after propagation delay.
Sequential circuit
Stores state. Flip-flops and registers hold values and update according to clock events.
Why both are needed
• The ALU computes an arithmetic result using combinational logic.
• The register file and program counter preserve CPU state.
• Feedback and clocked storage let a processor execute a sequence of instructions.

## Slide 10
M4 — Clocking and state in the CPU
CO4
DESIGN & SIMULATION OF MICROPROCESSORS | 10
Illustrative instruction sequence
Fetch
→
Decode
→
Execute
→
Write-back
Clocked state
At an active clock edge, state elements capture selected values according to their design.
Full-adder timing
The full adder does not need a clock. Its outputs settle after the input changes; the CPU may capture the result in a register.
Setup and hold time are important timing constraints for reliable register operation.

## Slide 11
M5 — Half adder vs full adder
CO5
DESIGN & SIMULATION OF MICROPROCESSORS | 11
Half adder
Inputs: A, B Outputs: Sum, Carry Sum = A XOR B Carry = A AND B
Full adder
Inputs: A, B, Cin Outputs: Sum, Cout Adds three one-bit values and includes carry from the previous stage.
Why carry-in matters
It allows multiple full adders to be chained for multi-bit arithmetic.
The carry from a less-significant bit becomes the carry-in for the next bit.

## Slide 12
M5 — Full-adder Boolean expressions
CO5
DESIGN & SIMULATION OF MICROPROCESSORS | 12
Sum
S = A ⊕ B ⊕ Cin
Carry-out
Cout = AB + ACin + BCin
Gate implementation
• P = A XOR B
• Sum = P XOR Cin
• C1 = A AND B; C2 = P AND Cin
• Cout = C1 OR C2
Components
2 XOR gates 2 AND gates 1 OR gate
Boolean symbols: ⊕ means XOR, · means AND, and + means OR.

## Slide 13
M5 — Truth table and worked example
CO5
DESIGN & SIMULATION OF MICROPROCESSORS | 13
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Example: 1 + 1 + 0
Sum = 0, Cout = 1 Binary result: 10₂
Example: 1 + 1 + 1
Sum = 1, Cout = 1 Binary result: 11₂ = 3₁₀

## Slide 14
M5 — Ripple-carry adder and subtraction
CO5
DESIGN & SIMULATION OF MICROPROCESSORS | 14
Full adder bit 0
carry
Full adder bit 1
carry
Full adder bit 2
carry
Full adder bit 3
Subtraction using two's complement
A − B = A + NOT(B) + 1
• Invert each bit of B and set the initial carry-in to 1.
• Reuse adder hardware for both addition and subtraction.
• Carry propagation creates delay as the number of bit stages grows.

## Slide 15
M6 — Logic gates and Boolean algebra
CO6
DESIGN & SIMULATION OF MICROPROCESSORS | 15
AND
1 only when both inputs are 1
OR
1 when either input is 1
NOT
Inverts the input
XOR
1 when inputs differ
NAND
NOT(AND); universal gate
NOR
NOT(OR); universal gate
Truth tables and Boolean algebra convert the full-adder behavior into a network of gates.
Sum-of-products is one systematic way to derive a circuit from a truth table.

## Slide 16
M6 — Universal gates and physical bits
CO6
DESIGN & SIMULATION OF MICROPROCESSORS | 16
NAND universality
Any Boolean function can be built using NAND gates alone. This offers an alternative implementation of full-adder logic.
Physical foundation
Logic 0 and logic 1 correspond to voltage ranges in a circuit. Transistors are used to implement practical logic gates.
Conceptual decomposition
CPU
→
ALU
→
Adder
→
Gates
→
Transistors
Opening each layer connects high-level processor behavior to physical logic.

## Slide 17
Simulation using Logisim Evolution
LAB
DESIGN & SIMULATION OF MICROPROCESSORS | 17
1
1. Create
Start a new circuit named FullAdder.
2
2. Place
Add input pins A, B, Cin and output pins Sum, Cout.
3
3. Build
Use 2 XOR, 2 AND, and 1 OR gate.
4
4. Wire
Connect gates according to the Boolean equations.
5
5. Test
Toggle inputs and check all 8 combinations against the truth table.
Expected result
All eight output combinations match the truth table.

## Slide 18
Simulation results and verification
LAB
DESIGN & SIMULATION OF MICROPROCESSORS | 18
• Test case 000 → Sum 0, Cout 0
• Test case 011 → Sum 0, Cout 1
• Test case 101 → Sum 0, Cout 1
• Test case 111 → Sum 1, Cout 1
• Verify the remaining four cases as well; the complete truth table contains eight input combinations.
• Record simulator screenshots showing inputs and outputs for your lab report.
Verification criterion
Observed Sum and Cout must equal the expected truth-table values for every test.

## Slide 19
Integration, extensions, and applications
EXTEND
DESIGN & SIMULATION OF MICROPROCESSORS | 19
ALU integration
The adder is used for arithmetic operations inside the CPU datapath.
Wider arithmetic
Connect multiple full adders to build 4-bit, 8-bit, or wider adders.
Applications
Microcontrollers, embedded systems, VLSI, and digital signal-processing hardware.
• Extend the ALU with another operation, such as XOR, by updating datapath and control logic.
• Connect a memory-mapped output peripheral to let the CPU control LEDs or a display.
• Performance depends on circuit delay, clock period, architecture, and other datapath components.

## Slide 20
Conclusion and references
SUMMARY
DESIGN & SIMULATION OF MICROPROCESSORS | 20
• M1–M2: understand the RISC-V CPU and locate the ALU in the datapath.
• M3–M4: understand operand storage, state, and clocked sequencing.
• M5: design the full adder, derive its equations, and build multi-bit arithmetic.
• M6: reduce the design to gates and understand their physical basis.
• Simulation verifies the design by checking all eight possible input combinations.
References
RISC-V International: RISC-V specifications Logisim Evolution: project documentation Digital Design and Computer Architecture — Harris & Harris
THANK YOU • Questions?